INSTRUCTION FOR RADIO OPERATORS ARRIVING AT SHELTERS

Revised 19 Dec. 2012

When a shelter is opened for a hurricane or other emergency event, the assigned radio operator should carry out the following,

- Check in with the shelter manager. The shelter manager could be a Red Cross representative, a Brevard County Supervisor assigned to a Special Needs shelter, or could be the school principal.

- If possible meet with the shelter manager and the staff as soon as the shelter opens, even

if you do not have your equipment ready. Advise them that you are there to provide

backup communication between the shelter and the EOC and/or the Red Cross HQ in

Rockledge, through an intermediate net control.

- With the managers agreement select an operating position close to where the shelter manager will be located.

- You need to try to get an antenna outside the shelter if you can, which means you need to be in a room with an outside wall and possible a window.

- It is important to get to the shelter early to secure your operating position before the shelter residents fill up the space. Shelters can open many hours before a hurricane arrives.

- The radio operator should be on site well before the storm arrives with his equipment set up.

- Also there is usually a sign in book for volunteers. This is important for staffing and for feeding, getting credit for operating and occasionally for workers compensation qualification (especially if it is a Govt. run site).

- After equipment setup, check in with net control to make sure you have a good signal into

the repeater. If you do not have adequate equipment, check into net control and tell them

what you are missing. It may be possible to provide the missing item(s).

- If there is little radio traffic and with the permission of the NCS see how many other local repeaters you can communicate with. Also do a simplex check into net control and the other shelters around you. This is important if the repeaters go down during or after the storm and you

have to relay a message thru another shelter to net control. Write this information down,

because another operator who was not involved in the simplex check may replace you at

some time.

- Have as many charged batteries as possible in case you lose commercial or generator

power. Plan for the worst.

- Don’t forget about the personal supply list: food, water, bed roll, spare batteries, etc.

- If you agreed to operate for a specific time or shift period and your relief arrives, step

down and allow the replacement to take over. No purpose is served by remaining at the

operating position longer than scheduled. You will have fulfilled your obligation and can

take a break. In addition you could upset your relief who is giving his/her time to

assist and expects to start his/her shift at an appointed time.

AB4ET